## Slide 1: River Discharge and Flood Hydrographs
Objective: To understand the characteristics of a storm Hydrograph in order to analyse and interpret their data.

## Slide 2: What is discharge?
Discharge = is the volume of water in a river, at a given place and time. It is calculated in cumecs (cubic metres per second).
Discharge = velocity x area.
Velocity = is the speed of the river (m/s)
Area = is the area of the cross section at a single point in the river (width x depth)

## Slide 3: What would cause a rivers discharge to ……
Increase?
Decrease?
Heavy rainfall
Long periods of rainfall
Urban areas (land use)
Impermeable rock (does NOT let water through e.g clay, slate.)
Saturated soils
Steep gradient
Low temperatures
Surface run off
Snow melt
No/little rainfall
Trees/vegetation (intercepts and takes in water)
Permeable rocks e.g limestone, chalk.
Porous rocks
Gentle gradient
Dry soils

## Slide 4: A flood/storm hydrograph
A rivers discharge can increase dramatically during and after a storm, causing flooding. It can also drop quickly after the storm has passed.
These changes can be recorded in a storm/flood hydrograph.

## Slide 5: A flood/storm hydrograph

## Slide 6
0 12 24 36 48 30 72
Hours from start of rain storm
3
2
1
Discharge (m3/s)
mm
2
3
4
Rainfall shown in mm, as a bar graph
Discharge in m3/s, as a line graph
Peak flow
Rising limb
Recession limb
Basin lag time

## Slide 7: Key words associated with a flood hydrograph. (You need to refer to these in exam questions about hydrographs)
Rising limb =
Falling limb (recession) =
Lag time =
Peak Flow =
Base flow =
The normal discharge of the river
Maximum discharge in the river
The flood water falling
The rising flood water in the river
The time difference between the peak rainfall and the peak discharge

## Slide 8
What affects the shape of a hydrograph?
Short Lag time
Long Lag time
Geology and soil
Land use
Type and amount of precipitation
Drainage density
Gradient of the valley sides

## Slide 10
How would tributaries affect
a storm hydrograph?
A
B

## Slide 11
Who would use hydrographs?
(and for what purpose?)